ESD Auto Inspection Robot
Software documentation details
Date: 17/10/2024

---
Software architecture
Pyqt5
- User Interface
- Control Test Flow
ROS 2: Humble
- Hardware Control
-Hardware Monitoring
Users
Hardware
All others folders outside of documentation and Interface_test_code
Code folder/files:
gui/
gui/RosNode/

---
Pyqt5 architecture
It is a single window application, the menu can open additional control window but the main logic are all store in the main window.
 1- window.py :
Event handling of the window movement, resizing or change
2- main_window.py:
- Initialize software with the function: setupSoftware()
- Controller logic in it (All button and signal handling)
3- main_layout.py:
- Initialize all graphical instance.
4- Others folders:
- RosNode/ contains interface for pyqt5 and ros2 system
- Others folders contains the layouts and widgets class separate by concern
ROS2 build needed files. Inside are information about the main file, licensing and dependency

---
Pyqt5 overall UI layout organization
I only put the main layout to control. Some intermediate layout are only for auto resizing purpose with widget and don’t have implication on the visual
MainWindowWidget (Qwidget): main_layout.py l.33
Object name (Object type): code localization
header_layout (QHBoxLayout): main_layout.py l.53
body_layout (QHBoxLayout): main_layout.py l.88
work_layout (QverticalLayout): main_layout.py l.148
controller_layout (QverticalLayout): main_layout.py l.103
Details of the controller and work layout are in slide 5/6/7

---
Pyqt5 Controller layout details
DESCRIPTION	CODE FILE
Fill information that can be query during test session for database upload	LG_TV_Information/layout/ModelInformationLayout.py
Control the brightness of LED system on the end effector. [Currently use LED is not recommended as it decreases AI detection and create reflection on TV]	LEDControl/layout/ControlLEDLayout.py
Control the brush actuator, with two possibility: unfold and fold at max and min value.	BrushControl/layout/BrushControlLayout.py
Control the TV with IR remoter command: turn on/off button, volume up, volume down	TVControl/layout/ControlTVLayout.py
Start test session. Currently 2 modes available: / DEMO: cross-over/ test one preset connectics with air/ cross over / AUTO: automatic scan of the TV/ sorting of the found value/ test with air/contact of all of them (+tooltip change)	RobotTest/layout/ControlButtonLayout.py

---
Pyqt5 work widget: test layout details
DESCRIPTION	CODE FILE
Hand-eyes camera with AI detection model apply in real-time & front camera image. / Only monitoring, no interaction possible	CameraViewer/layout/FixCameraDetectionLayout.py
Information about the test points detected. Empty when start software. When we run a test sequence, the results of the detection part will show. The user can remove unwanted points from the table	PartsDetection/layout/PartsDetectionLayout.py
Information about the ESD test. Empty when software start. When we are in esd test part, the line are added in real-time when we are doing one test item. First with testing then with the results OK, NG	ResultsManager/layout/TestTableFullLayout.py
Monitoring of the defect detection camera with the screen state (black-screen or turn on) in real-time with AI model. The defectLog is extra details about the defect detected when testing parts	DefectDetection/layout/DefectCameraDetectionLayout.py

---
Pyqt5 work widget: configuration layout details
DESCRIPTION	CODE FILE
List of the Test Points to detect on the TV with the associate category to test on it. The in sequence column is not functional yet, but in future you can use it to enable/disable some points to test	ConfigurationTest/layout/ConfigurationLayout.py / Line 31
Configuration for the auto sequence, LED light, brush movement, TV front number of points, tv back.	ConfigurationTest/layout/AutoSequenceLayout.py
List of the test to do for a category: ID is for database upload, Mode for defect detection, discharge number and voltage for the esd test.	ConfigurationTest/layout/ConfigurationLayout.py
These parameters can be change in administrator mode only. (Also if you save them, they will be apply as default value for next software run)

---
Software: Test main logic
When we click on the test start button, the selected test will be launch (I.e auto or demo test). Each test case is a Qthread so it can run parallel to the main window update
 1- DemoSequenceThread
- Crossover of the TV
- Test 1 preset points in air with +15 / -15 Volt
- Return back home
2- AutoSequenceThread
- Detection of test parts on TV
- Automatic test of all the detected points
main_window.py

---
Test: Auto sequence initialization
The Qthread is an custom object name AutoSequenceThread. When create the object, the function __Init__() is run which initialize the variable. Then we connect all the necessary pyqt5 signal to communicate between the main window thread and the test thread safely. When we start the thread the run() function is executed.
The run function is execute in the Thread until the end of the function.
The self.exec_() function makes the thread pauses until a self.quit() function is called in the Thread.

---
Test: Auto sequence initialization
The Qthread is an custom object name AutoSequenceThread. When create the object, the function __Init__() is run which initialize the variable. Then we connect all the necessary pyqt5 signal to communicate between the main window thread and the test thread safely. When we start the thread the run() function is executed.
The run function is execute in the Thread until the end of the function.
The self.exec_() function makes the thread pauses until a self.quit() function is called in the Thread.

---
Pop Up window system
- PopUpProtectionLED.py: when the admin is trying to put the maximum value for the LED system (G)
- PopUpTesting.py: when we are running a test and the user try to change the robot/system setting or run another command
- PopUpResetGantry.py: when we use the manual gantry command control, the collision with the TV is disable. So the pop up remind the user to check if the movement is possible before.

---
ROS2 architecture

---
Additional ressource
ROS2 tutorial start:
https://docs.ros.org/en/humble/Tutorials/Beginner-CLI-Tools/Understanding-ROS2-Nodes/Understanding-ROS2-Nodes.html